## Slide 1
Hands on Workshop:
Getting Started with RF Design of Wireless Systems
Sekhar Sekharan, PhD
MathWorks Inc.

## Slide 2: Agenda
Use a practical example to understand the basics of analysis and simulation technology
  Analyze the RF budget of a receiver starting from high-level specifications
  Integrate the antenna and simulate the impact of interfering signals and polarization mismatch
  Design a dual polarized antenna and its feed network on a PCB and integrate it in the receiver
Expected learning outcomes:
  Validate simulation results using different RF analysis tools
  Integrate datasheet specifications and measured data to improve modeling fidelity
  Create executable models from antenna to bits including: dispersion, impedance mismatches, coupling, polarization, non-linearity, noise, interferers

## Slide 3: Practical Example: Design of a ZigBee Receiver Using RF Components
Start from the system specifications and build an executable model
Explore the architecture, refine the RF front-end design, integrate the antenna
Validate the system behavior in presence of interfering signals
?
https://www.mathworks.com/help/simrf/ug/top-down-design-of-an-rf-receiver.html

## Slide 4: Reference Testbench: Baseband Signal Processing + RF Receiver
Desired Signal
@2.45GHz
Interfering Signal
@2.5GHz
Direct conversion
RF receiver
ADC placeholder
Baseband receiver
ChER measurement
DC offset correction

## Slide 5: Part 1: RF Design – Where To Start? RF Budget Analysis

## Slide 6: Exercise 1: RF Budget Design and Analysis
1. RF chain budget analysis
2. RF chain Harmonic Balance analysis

## Slide 7: RF Design – Where To Start?
RF Budget Analyzer App
Compute and visualize power/noise/IP3 RF budget with Friis and Harmonic Balance
Improve over spreadsheet analysis: account for impedance mismatch and high-order nonlinearity
Generate MATLAB scripts for automation and complex scenario analysis
Generate Circuit Envelope models/testbenches for simulation and system integration

## Slide 8: Analyze, Understand, and Debug RF Data and RF Budget
RF components
Export to MATLAB / RF Blockset
Cascaded Budget Analysis (Friis and Harmonic Balance)
Visualization
Harmonic Balance (non-linear) analysis
System specifications
Notes: You can describe any arbitrary RF chains for transmitter and receivers, and identify the most critical components by analysing the noise and power budget.

## Slide 9: Exercise 1

## Slide 10: Friis Formulas, Deceptively Easy!
What about impedance mismatches?
What happens with modulators/demodulator?
What happens if one of the stages is close to saturation?
What happens to second order nonlinearity?
G1
F1
IP3_1
G2
F2
IP3_2
G3
F3
IP3_3
G4
F4
IP3_4
Notes: These are Friis formulas.
According to Friis every RF components can be treated like an amplifier, and if the operating range is mildly nonlinear then everything works fine.
These formulas are often implemented in Excel spreadsheet, and have often major limitations.
For example, what happens to impedance mismatches, or what happens to components that change the signal frequency, like modulators, or to effects that generate harmonics out of band? These are hard questions to answer with these ideal formulas.

## Slide 11: What is Harmonic Balance?
Accurate non-linear analysis
  Sinusoidal tones
  Steady state conditions
  Mild non-linear circuits
Now available in RF Budget Analyzer app
Foundation of RF Blockset Circuit Envelope simulation
Notes: Harmonic balance is an analysis technique used to improve the accuracy of RF analysis.
It is based on a few sinusoidal tones, and operates only in steady state conditions. Ofrget about using HB with feedback loops and adaptive systems!
Major analysis tool of Keysight ADS used for RF design at the transistor levele, where time domain simulation or even circuit envelope is too time consuming.
Easy to include linear frequency-defined components
  S-parameters, distributed elements (microstrips, coplanar waveguides, …)
Good for (mildly) non-linear circuits
  Complexity increases exponentially with the number of independent input tones
Before adding HB in the app, results were only computed with Fris.
This means that now results are more accurate, and it opens up fir further improvements along the way.

## Slide 12: Part 2: RF System Simulation

## Slide 13: Exercise 2: RF System Simulation and Model Integration
1. RF chain budget analysis
2. RF architectural model
3. RF system integration and simulation
non-linearity, noise, and interfering signals

## Slide 14: Export from RF Budget Analyzer
MATLAB workspace object
  Bidirectional workflow between app and command line
MATLAB script
  Automate corner analysis and chain optimization
RF Blockset
  Generate model for Circuit Envelope simulation
  Automatic configuration of Input/output ports
Measurement testbench
  Measure gain, noise, IP3, IP2, DC offset, and image rejection
rfsystem
  Integrate RF model directly in MATLAB for simulation

## Slide 15: Tradeoff Modeling Fidelity and Simulation Speed
Models at high levels of abstraction
Solvers that use larger time-step

## Slide 16: Control the Simulation Set-Up and Complexity
Freq 1
freq
Spectrum
Freq 2
DC
Envelope bandwidth = 1 / time step
Number of mixing products
depends on harmonic order

## Slide 17: Circuit Envelope Available Blocks
Frequency dependent (linear) elements
  S-parameters, antenna, filter, attenuator, coupler, circulator, divider/combiner, phase shifter, RLC, transmission lines
Nonlinear elements
  Amplifier: polynomial, generalized memory poly, AM/AM-AM/PM table
  Mixer: polynomial, IM table, and complete modulator/demodulators
Noise generation included for linear and non-linear elements
  Thermal noise (white and colored)
  Phase noise
Variable (Simulink controlled) elements for tunable networks
  Non-linear variable gain amplifier, variable attenuator, bidirectional variable phase shifter, variable RLC

## Slide 18: Direct Conversion Demodulation
2.45GHz
frequency
Desired signal
Local Oscillator
2.45GHz
0Hz
Desired signal
Channel select filter
frequency

## Slide 19: Direct Conversion Demodulation and Reciprocal Mixing
2.45GHz
frequency
Desired signal
Local Oscillator
2.45GHz
0Hz
Desired signal
Channel select filter
Local Oscillator leakage
Local Oscillator self-mixing
Finite isolation
frequency

## Slide 20: Direct Conversion Demodulation and Interfering Signals
2.45GHz
2.5GHz
frequency
Desired signal
Interfering signal
Local Oscillator
2.45GHz
0Hz
50MHz
Interfering signal
Channel select filter
frequency
Desired signal

## Slide 21: Direct Conversion Demodulation and Interfering Signals
2.45GHz
2.5GHz
frequency
Desired signal
Interfering signal
Local Oscillator
2.45GHz
0Hz
Finite IP2
Channel select filter
Interfering signal
2nd order harmonic
Desired signal
frequency
50MHz
Interfering signal

## Slide 22: When to Use MATLAB, When To Use Simulink? Use rfsystem to wrap an RF Circuit Envelope model for simulation in MATLAB
Create rfsystem object
from budget analysis
Use Circuit Envelope model as part of a MATLAB testbench

## Slide 23: Part 3: Antenna Design and Analysis - Where to Start? Estimating the Impact of Antennas on Your System Performance

## Slide 24: Exercise 3: Antenna Design, Analysis, and Integration
2. RF architectural model
3. Antenna integration:
impendance, directivity, polarization
1. Antenna analysis

## Slide 25: Design, Analyze, and Visualize Antennas
Get started with antenna and array catalog and apps
Perform full-wave EM simulation (Method of Moments)
Improve the performance using surrogate optimization
Design and fabricate PCBs with Gerber file generation
Analyze the effects of installation on large platforms
Include RF propagation effects
Notes: Antenna Toolbox offers a lot more than what discussed today, such as surrogate optimization, PCB design, installation of antennas on platforms and the analysis of propagation effects.

## Slide 26: Antenna Design – Where To Start?
Antenna Designer / Array Designer / PCB Antenna Designer Apps
Select an antenna/array based on the desired specifications
Design the antenna at the operating frequency
Visualize results and iterate on antenna geometrical properties
Generate MATLAB scripts for automation
Notes: When ew developed Antenna Toolbox, we had 1 objective in mind: make Antenna design and analysis easy for the non-EM expert.
While making complex things possible for the experts.

## Slide 27: Designing your First Antenna
p = design(patchMicrostrip, 70e9);
impedance(p, (69.5e9:50e6:70.5e9));
current(p, 70e9);
pattern(p, 70e9,0 (-180:5:180));
g = fractalGasket
g.NumIterations = 4
s = sparameters(g, ...
linspace(800e6, 1.2e9, 20))
rfplot(s)
l = design(linearArray,70e9, ... patchMicrostripCircular)
pattern(l, 70e9)

## Slide 28: Exercise 3

## Slide 29: Antennas Recently Added to the Catalog
Ridged waveguide
Corrugated horn
Fractal snowflake
Elliptical patch
Monocone
Tapered LPDA
Antipodal Vivaldi
Vivaldi offset cavity
Rectangular DRA
Egg Crate Vivaldi
Cylindrical DRA

## Slide 30: Antenna Electromagnetic Analysis
Full-wave solver: Method of Moments
Analysis-driven automatic mesh generation: triangles for surface, tetrahedra for volume
  Manual control on meshing for advanced use cases
Support of dielectric and metal materials
Validated against state-of-the-art results
Notes: RF PCB Toolbox uses the method of moments to analyze the PCB structure.
The structure will be automatically meshed: triangles for the metal surfaces, and tetrahedra for the dielectric volume.
You have the ability to manually control the maximum, minimum edges of the mesh, as well as the growth rate from minimum to maximum.
With the MoM you can compute S-parameters, impedance (inductance and capacitance), as well as charge and current distribution.
If you design PCB antennas and you are interested in the far and near field performance, you can use Antenna Toolbox.
With the method of moments, you can take into account the impact of the material properties, such as dielectric losses and metal conductivity.
Results have been validated against state-of-the-art publications and measurements.

## Slide 31: Integration with Full-Wave EM Analysis for Antenna Design
Explicit modelling of polarization
Modeling of impedance, bandwidth, and frequency-dependent far-field radiation pattern

## Slide 32: Behind the Scenes: Integrate Antenna Array Modeling in RF Simulation
TXsignal (EIRP)
TX Array
S-parameters
Instantaneous voltage excitation to compute radiation pattern
Sarray
VTX
ITX
RXsignal
RX Array
S-parameters
Incident plane wave excitation to compute feed currents
Sarray
VRX
IRX
Antenna Toolbox array object or measured antenna object
Embedded element pattern used to compute the full-array pattern
Frequency dependent modeling of S-parameters and pattern
Multicarrier signals
Polarization effects
Direction of arrival and departure

## Slide 33: Measured Antenna Object
Import antenna data from measurements or 3rd party EM tools
  S-parameters
  E-field, embedded element
Integrate object into RF simulation and reflector analysis
P: No. of observation points
F: No. of frequency points
N: Number of ports
E: P X 3 X F
Direction: P X 3
embedded: P X 3 X F X N
Sparameters: sparameters object

## Slide 34: How Can AI Help?
Antenna design optimization
Use surrogate model assisted differential evolution for antenna synthesis (SADEA)
Use on optimization problems that are expensive to evaluate
Does not rely on gradients: works on smooth and nonsmooth problems
3D Pattern reconstruction
Use deep learning to reconstruct a 3-D antenna radiation pattern from two orthogonal 2-D slices
Reduce the time required for measurement or EM analysis of 3D patterns
Achieve more accurate interpolation than using analytical methods
https://www.mathworks.com/help/antenna/ug/antenna-optimization-algorithm.html
https://www.mathworks.com/help/antenna/ug/reconstruct-3d-pattern-from-2d-slices-using-deep-learning.html

## Slide 35: Part 4: Integrating Dispersive Components

## Slide 36: Exercise 4 and 5: Antenna Integration and Importing S-Parameters
2. RF architectural model
3. System integration:
impedance, coupling, dispersion
1. Planar component analysis

## Slide 37: RF PCB Components
Notes: This is a current snapshot of the RF PCB components that you will find in RF PCB Toolbox.
You can find the complete list here: https://www.mathworks.com/help/rfpcb/pcb-components-catalog.html

## Slide 38: Cascading PCB Components
Modular approach to building PCB assemblies
Automatic port assignments
Combine components (shapes) and antennas
+
+
=
c = design(couplerBranchline,2e9);
mc = design(coupledMicrostripLine,2e9);
mc.Spacing = c.ShuntArmLength;
w = design(wilkinsonSplitter,2e9);
r = pcbcascade(c,mc);
r = pcbcascade(r, w, 3, 1);
r = pcbcascade(r, w, 3, 1);
show(r)
Notes: You can create PCB assemblies by cascading PCB components.
The ports will be automatically assigned to match the structure.
This also works with antenna objects, for example to build feed and matching networks.
In this simple example we cascade a coupler, with a coupled microstrip line and two Wilkinson dividers.
This us a simple example of creating a feed network.

## Slide 39: Exercise 4

## Slide 40: Electromagnetic Analysis of PCB Structures
Full-wave solver: Method of Moments
Volumetric mesh of the PCB
  Analysis-driven automatic mesh generation
  Manual control on meshing
Specify material properties: metal and dielectric

## Slide 41: Coupling in Antenna Arrays: Near and Far Field Effects
RF Transmitter
S-parameters model near-field leakage in between elements
Patterns of elements embedded within an array differ from the isolated element
S-parameters
Embedded element #1
Embedded element #8

## Slide 42: Impact of Coupling on the Antenna Array Pattern
Without coupling
With coupling

## Slide 43: Impact of Coupling on Beamforming Algorithms
Example: beam and null steering for interferer mitigation
Beam at 15deg from boresight
Null at 45deg from boresight
Without coupling
Attenuation = 16.3+51.6 = 67.9dB
With coupling
Attenuation = 16.2+16.8 = 33dB

## Slide 44: Simulate In- And Out-of-Band Interfering Signals Model interference scenarios, sensing, and multi-standard coexistence
3GPP FR2 TM3.1
Desired signal @27GHz
Az El = [60 0]
Power = -70dBm
OFDM 100MHz BW
Interferer @19GHz (image frequency)
Az El = [40 0]
Power = -70dBm
FIN = 27GHz
FLO = 23GHz
FIF = 4GHz
FINTERF = 19GHz
~
~
~
20GHz
28GHz
FLO
Image rejection filter
FIF_INTERF = 4GHz
Finite isolation
With interfering signal RMS EVM = 4.2%
RMS EVM = 3.6%

## Slide 45: Exercise 5

## Slide 46: S-Parameters Analysis with RF Toolbox
Import, visualize, and export Touchstone files
Manipulate and analyze networks of RF components, including N-port S-parameters
Represent frequency-domain data using rational fitting for time-domain simulation

## Slide 47: What is Rational Fitting?
Equivalent expression given by a ratio of two polynomial functions
  Laplace domain model providing a state-space representation
  Equivalent to a pole-zero description of S-parameters
  Suitable for time-domain simulation (e.g. Spice-like, or RF Blockset circuit envelope)
Benefits:
  Simple model for given accuracy: model order reduction avoids overfitting of measurement noise
  Causal by construction: suitable for data interpolation/extrapolation and pulse response analysis
Residues
Poles
Direct feedthrough
(value at  frequency)
Time delay

## Slide 48: Sources of Dispersion and Impedance Mismatches
Amplifiers
Antennas impedance and pattern
Power amplifiers memory effects
Passive distributed elements

## Slide 49: Dispersion Affects Broadband Signals
Frequency dependent gain:
Amplitude and phase
Input: white noise
Output: frequency dependent gain

## Slide 50: Dispersion Requires Equalizer Compensation / Calibration
Baseband receiver
With equalizer
Without equalizer
Example: OFDM 100MHz Bandwidth modulated input signal
Static phase equalizer
Automatic gain control
1024 carriers
120kHz spacing
122.88MHz bandwidth
Notes: As the signal bandwidth is large the frequency response is not flat. This must be compensated.
In particular, gain flatness is ok, but there is an almost constant group delay leading to a 30degrees phase rotation over the 100MHz signal bandwidth.
If the TX is not equalized, a simple receiver will have a degraded EVM.
The equalizer in reality will not be in RX, but will be part of the TX, and it is essentially providing static calibration of the TX frequency dispersion.
As it is linear it can be moved in the TX chain with consistent results.

## Slide 51: Conclusions
We use a practical example to understand the basics of analysis and simulation technology
  Analyze the RF budget of a receiver starting from high-level specifications
  Integrate the antenna and simulate the impact of interfering signals and polarization mismatch
  Design a dual polarized antenna and its feed network on a PCB and integrate it in the receiver
What we learned:
  Validate results using different RF analysis tools: Friis, Harmonic Balance, Circuit Envelope
  Integrate datasheet specifications and measured data to improve modeling fidelity
  Create executable RF models including: dispersion, impedance mismatches, coupling, polarization, non-linearity, noise, interferers

## Slide 52: Extra: Modeling and Linearization of Power Amplifiers

## Slide 53: PA Linearization: Digital Pre-Distortion (DPD) in Theory
Pin [dBm]
Pout [dBm]
Linear characteristic
(desired)
PA characteristic
(actual)
Compression
DPD characteristic
PA
DPD
Notes: Let’s take a step back, and see how Digital Pre Distortion can be used to increase the transmitters linearity. The principle is simple: the Power Amplifier introduces non linearity, here described by a compressing characteristic in orange.
<click>
However, the desired TX characteristics should be linear, such as the black curve.
<click>
For this reason, we introduce a digital algorithm (Digital Pre Distortion) before the PA that pre-distorts the signal …
<click>
The DPD characteristic is the inverse of the one of the PA. The overall behaviour is linear even if both the elements are non-linear because their characteristics cancel each other.

## Slide 54: PA Linearization: Digital Pre-Distortion (DPD) in Practice
PA
DPD
Pin [dBm]
Pout [dBm]
PA characteristic
(actual)
Compression
Memory
RF
Baseband
Up-conversion
Down-conversion
Adaptive coefficients
Timing
Antenna loading
DPD characteristic
Notes: If the theory is simple, the practice of designing and implementing a DPD algorithm is far more complex.
First, the PA is not only non-linear, but it is also affected by memory. The output of the PA at a certain point in time also depends on the values of the input signal in the past. This means that the PA behaviour depends on the type of modulation, bandwidth, power, Peak to Average Power Ratio and other characteristics of the input signal.
For this reason, the DPD algorithm should be adaptive and has to operate in a closed feedback-loop configuration, to compensate for the PA effects.
To make things even more complex, DPD algorithms are digital algorithms implemented in baseband, while PAs are RF components operating at high-frequency. This means that up-conversion and down-conversion stages are required to make the two systems operate together.
All the low-power analog and RF components include imperfections that need to be considered as they will affect the DPD behaviour. Timing imperfections are important as they might make the system unstable. Other aspects that cannot be neglected are, for example, the loading effects of the antenna on the PA, or the DPD strategy to adaptively compute the corrections coefficients.

## Slide 55: Fitting Memory Polynomial Series with MATLAB
Simple, fast, customizable fitting procedure to model memory and non-linearity
Based on I/Q (time domain, wideband) measurement data from your PA
Generalized model including memory lead and lag terms with a causal response implementation
Degree of non-linearity
Memory length
Order 
Memory
length 
Notes: MATLAB can effectively help you in more easily identifying a PA model based on a generalized memory polynomial series as described in this IEEE paper from Dennis Morgan and others. The idea is straightforward: use input/output complex (I,Q – in phase and quadrature) characteristics of the PA to extract the coefficient matrix “a” describing the model.
<click>
M represents the memory depth.
<click>
K the degree of non-linearity.
This approach can also be used to describe purely static characteristics such as AM-AM/AM-PM, by setting the memory depth equal to 1.

## Slide 56: Using 3GPP Standard Signals
Reference BB transmitter
FR2 TM1.1
Reference BB receiver
FR2 TM1.1
rfsystem
RF Transmitter model
inWaveform
outWaveform

## Slide 57: Testing Transmitter Linearization
No DPD EVM RMS = 3.4797%
No DPD ACPR = 37dBc
With DPD ACPR = 45dBc
With DPD EVM RMS = 0.44591%

## Slide 58: Testing Transmitter Emissions
LO leakage (60dBc)
EIRP -15deg @23GHz
FIN = 4GHz
FLO = 23GHz
FOUT = 27GHz
Beamforming at 15deg
from boresight
EIRP 15deg @27GHz

## Slide 59: How Can AI Help?
AI for Digital Predistortion Design
Model, train, and test the following neural network architectures:
  Augmented real-valued time-delay neural network (ARVTDNN)
  Long short-term memory neural network LSTMNN)
  Bidirectional LSTM neural network (BiLSTMNN)
  Gated recurrent unit neural network (GRUNN)
Structurally compress neural network DPD: reduce computational complexity and memory requirements by using projection and principal component analysis
https://www.mathworks.com/help/comm/ug/ai-for-digital-predistortion-design.html
https://www.mathworks.com/help/comm/ug/power-amplifier-modeling-using-neural-networks.html